## Slide 1
FIRE FIGHTING DRONE
PROJECT
Presented By: Team AGNI Drone
Aryan
Tanmay
Parth
Jainil
Vansh
Mayank

## Slide 2
OUR PROJECT TIMELINE
PLANNING
PRE-DESIGN
DEVELOPMENT
TESTING
To make this assembly we have used PVC pipes with T and Plus joints and for Moter we used custom 3D Printed motor Mounts.
  Total Flight Time: Nearly 2 hours in around 24 test flights.
  Height achieved: Successfully lifted the water up to 10m of height
Strategic Goals
Implementation
Quality Assurance
Created CAD layouts for a hexacopter frame to check stress distribution. Finalized specs for tubing diameter, pump flow rate and battery capacity to balance weight, thrust and firefighting payload requirements.
Blueprint Creation
First to built a simple quadcopter using the Cross Flight flight controller to gain basic flight experience. Conducted component research to identify motors, ESCs, props and a lightweight frame capable of carrying a water-pipe assembly in final Hexacopter drone model.

## Slide 3
DRONE COMPONENTS
03
  Initial Learning Phase
    We initially planned to build this heavy lift drone in multiple stages
    Started by studying a already available quadcopter F450 frame .
  Exploration and Inspiration
    Found an H-type quadcopter design online.
    Took inspiration from the H-type structure for better stability.
  Design Modification
    Modified the H-type quadcopter frame into a hexacopter frame.
    Increased motor count for improved load handling.
    One feature we believe sets our design apart from others is that it can be assembled without using a single screw.
  Configuration Choice
    Adopted a Plus (+) type configuration for the hexacopter because it has better control on movement of drone at slower speeds.
  Performance Considerations
    Plus type has slightly higher aerodynamic drag.
    Drag increase is acceptable due to our low-speed application.
    Gains in stability and easier control outweigh the minor drag penalty.
FRAME
01
F450 Frame
Our Design Inspiration
Final Design of Our Prototype

## Slide 4
DRONE COMPONENTS
FLIGHT CONTROLLER
03
02
03
  Built-In Sensors: 6-axis IMU (3 Axis Accelerometer + 3 Axis Gyroscope), Barometer and Magnetometer keep your hexacopter level and aware of altitude and heading.
  Auto-tune, in-flight parameter adjustment(PID Tuning), mission scripting.
  Hexacopter-Ready I/O: Up to 8 motor outputs plus ports for GPS, Telemetry radios, RC receiver and additional sensors—all on one board.
  Smart Failsafes: Auto Return-to-Launch, auto-land on low battery or signal loss, and real-time power monitoring to protect your drone.
  Seamless integration with Mission Planner(PC), QGroundControl(Mobile), MAVProxy software, for Sensor Calibration and Tuning.
  It also enables us to do Autonomous flights with some sensor integration and software settings.
Image Source: https://encr.pw/fQeDP

## Slide 5
DRONE COMPONENTS
03
ELECTRONIC SPEED CONTROLLERS (ESCS)
03
  Working of ESC
    Control the speed and direction of the motor by supplying power to them.
  Specification of chosen Hobbywing XRotor 40A 2-6s ESC :
    Provides a continuous current of 40 A with a peak current of 60 A.
    It has a throttle signal frequency up to 621Hz.
  This ESC supports 2s to 6s batteries.
  smooth throttle response, protection circuits and is very efficient.
  it’s PWM(Pulse Width Modulation) signal give finer resolution control for flight controllers
https://robokits.co.in/multirotor-spare-parts/brushless-motor-propeller-esc/esc/hobbywing-xrotor-40a-2-6s-esc

## Slide 6
DRONE COMPONENTS
03
BATTERY
04
  Working of Battery:
    Provide the power necessary for extended flight durations.
  Specification of chosen Tattu 10000mAh 6S 25C 22.2V LiPo battery :
    Provides a capacity of 10000mAh (10Ah) with 22.2 V voltage drop.
    It has a discharge rate of 25C and a max burst discharge Rate: 50C
    It weights around 1420g.
    it has a maximum continuos current of 250 Amps
    Flight time is around 15 to 20 minutes.
  This Battery is a 6s battery that supports an ESC.
  The motor in this drone is optimized for 6 S (≈ 22.2 V) operation, providing 320 RPM/Volt to generate 1.3–1.5 kg thrust per motor.
https://robokits.co.in/batteries-chargers/drone-batteries/tattu-lipo-batteries/tattu-6s-battery/tattu-10000mah-6s-25c-22.2v-lipo-battery

## Slide 7
DRONE COMPONENTS
03
  Tarot 4114/320KV Brushless Motor
  Purpose: Provides strong lift and stable performance for hexacopters carrying heavy payloads (pipe and water).
    Thrust
    Each motor's weight is 148 grams. We choose lightweight motors for heavy lift applications.
    Each motor with a (15-inch propeller) can produce around 1.8 kg at 80% thrust. Motor speed is 5511 RPM. The total thrust is 10.8 kg. The total drone weight is near with pipe nearly 4.5 kg without water. So it can easily carry water through the pipe.
    According to this thrust requirement, we selected 15-inch diameter propellers by considering Tarot 1441/320 KV Brushless motor.
    Material Properties
    This tarot motor is made of an alloy steel shaft, and the special bearings are used for low friction.
MOTORS
05
Tarot 4114/320KV Brushless Motor
Stator Size: 41X14 mm

## Slide 8
DRONE COMPONENTS
03
  Tarot 4114/320KV Brushless Motor
    Properties
      Stator gives better heat dissipation means the motor can release this heat faster into the air — cooling itself down more effectively.
      Better heat dissipation helps the motor stay cool, improving performance, efficiency, and durability during heavy flights
      320KV motors (KV tells you how fast the motor spins when you apply 1 Volt with no load.) are lower KV motors it gives more torque, less speed and it is selected according to large propellers, and stability.
MOTORS
05
Tarot 4114/320KV Brushless Motor

## Slide 9
DRONE COMPONENTS
03
  Propeller
    The drone required significant thrust and efficiency, so considering this, we selected a 15-inch diameter(5.5 inch pitch) size propeller also according to our prototype. So the propellers can't collide with each other.
    Both types of propellers used CW and CCW.
    Propeller's material is carbon fibre, which is strong, lightweight and highly durable. Carbon fibre reduces flexing at high RPM and maintains propeller shape.
    The propeller's large size and light weight (40g/propeller) give better lift, lower power consumption and improve flight time.
PROPELLERS
06
Carbon Fibre Propellers

## Slide 10
Maximum Height upto which the Drone can Go while carrying water
  Thrust Provided at 80 % Throttle = 1.8 kg per motor
  Total Thrust = 1.8 X 6 = 10.8 kg
  Mass of Drone Itself = 4.5 kg
  This Extra thrust would be responsible to carry weight of pipe and water (which is depend of Height of Drone )
  We did the Calculation using Density and Volume of common garden Pipe material and water inside it.
  We found out that Theoretically the Drone can go upto 22 m or 70 Feet of Height while carrying water.

## Slide 11
Maximum Velocity and Volume Flow Rate that can be kept while Spraying Water.
As We Spray water by attaching a pipe , a Thrust Force due to Water is Experienced by the Drone.
This Thrust force should not be greater than the maximum Forward force the Drone provides.
Thus using this information , we found the
  Maximum Velocity of Water = 7.5 m/s
  Maximum Volume FLow rate = 2.5 L/s or 150 L/min

## Slide 12
  Device: Skydroid T10 Remote Controller (Handheld device)
  Function: Sends control signals (joystick inputs, switches, and buttons) to the drone or vehicle.
  Features:
RECEIVER AND TRANSMITTER
07
TRANSMITTER
  10 channels (physical control channels) to which we can assign different functions
  Antenna: 2.4 GHz 3 dB built-in antenna
  App Integration: Bluetooth connectivity for parameter adjustments, channel binding, failsafe settings, and firmware upgrades via the Device Helper mobile App
  Send commands 300 times per second
  Device: Skydroid R10 Mini Receiver (Drone-mounted device)
  Function: Receives control signals from the transmitter and sends telemetry data back to the ground station.
  Features:
  Dual 2.4 GHz antennas for strong, stable signal reception
  Binding button and LED indicators for easy connection and status monitoring
  Supports Bluetooth firmware updates via Device Helper app
RECEIVER
  Digital Video Link: Up to 7 km line-of-sight
  Data & Telemetry Link: Up to 10 km line-of-sight

## Slide 13
🔹 Basic Working Principle
  GPS Functionality:
    Receives satellite signals from multiple constellations (GPS, GLONASS, Galileo, BeiDou).
    Calculates precise 3D position (latitude, longitude, altitude) by triangulating distance from satellites.
    Uses WGS-84 coordinate system for mapping locations.
  Compass (Magnetometer) Functionality:
    Measures Earth’s magnetic field to determine heading (orientation of the drone).
    Assists in stable direction control and Return-to-Home (RTH) navigation.
  Flight Controller Interface:
    Sends GPS position and compass heading data to Pixhawk via serial communication.
    Enables real-time navigation, waypoint tracking, and autonomous flight.
NEO-M8N READYTOSKY GPS
08

## Slide 14
DRONE COMPONENTS
POWER DISTRIBUTION CHART
09

## Slide 15
DRONE COMPONENTS
  Battery to ESC’s through PDB :
    The main battery’s (LiPo battery) two wires are directly soldered or connected via connectors to the input VSS and GND of the Power Distribution Board (PDB) for powering esc through the VSS output sets (for our quad drone) of output pads for each ESC getting same voltage (Parallel connection).
  Power to Flight Controller and Receiver:
    We have used a 1 x Power Module: PM02 V3 12S .
    PM02 V3 acts as a power module for Pixhawk with safe 5.2V supply. it also Monitors Battery Voltage and Battery Current (This data is sent to the Pixhawk for battery percent, consumption, warnings)
    In our Quad drone we have used cross flight Power module to power ESC and FLight controller.
POWER DISTRIBUTION
10

## Slide 16
DRONE COMPONENTS
3-D PRINTED AND LASER CUT PARTS
11
Designed using Autodesk Inventor and Fusion 360
  Total 6 motor holders Securely mount the motors onto the drone frame.
  Filament Type: Tough Red PLA
  Print Core: AA 0.4
  Infill Density: 20% ( for reducing the weight of the component)
  Infill Pattern: Triangles ( very high strength to density ratio)
  Mass per Motor Holder: 34 grams
The 3-D printed support plate was used to hold the electronic components (like flight controller, receiver and Battery)
Features of the Parallel Vents in the Plate:
  Air Ventilation: Allows smooth airflow through the plate to prevent unwanted thrust or turbulence and improve stablity.
  Component Centering and Support: Helps securely hold and align components at the center of the drone.

## Slide 17
DRONE
SUB-COMPONENTS
03
WIRES AND CONNECTORS
VIBRATION DAMPERS
01
02
01
SAFETY BUTTON
03
ANTENNA
MOUNTING HARDWARE
05
04
BATTRY CHARGER
06

## Slide 18
DRONE
SUB-COMPONENTS
03
LIPO-CHECKER
01
07
GPS MOUNT
08
SD-CARD
09
BUZZER
10

## Slide 19
https://iitgnacin-my.sharepoint.com/:v:/g/personal/23110300_iitgn_ac_in/EXxrx1mxkjNOrGBSVK1xQfgBHd3mzywUZGAm6lMl7FmELg?e=0giEab
TESTING VIDEO

## Slide 21
THANK YOU
THANK YOU